## Slide 1
SYNTHETIC GPR REBAR INVERSION
Recovering rebar geometry from radar waveforms
A mature FDTD / full-waveform-inversion pipeline that recovers a 3-rebar variable-depth, variable-radius scene under noise, source mismatch and ringdown stress — with honest confidence reporting.
425/425
exact geometry recovered
740–1218
output runs evaluated
synthetic
not yet field-validated

## Slide 2
THE PROBLEM
Find hidden rebar from a single radar trace
Ground-penetrating radar sees concrete from the surface. We want each rebar's horizontal position (x), depth (z) and radius (r) — but the only measurement is the reflected waveform.
Forward model: FDTD
Finite-difference time-domain simulation turns any candidate concrete/rebar scene into a synthetic radar waveform.
Inverse model: FWI
The optimizer never sees the truth. It proposes scenes and keeps the one whose simulated waveform best matches the reference.
Three synthetic rebars
target0 (150, 80, r5) · target1 (250, 100, r6) · target2 (350, 120, r8), in millimetres.
THE OPTIMIZER LOOP
1
Propose a candidate scene
guess x, z, r in bounded windows
2
Simulate its waveform
run FDTD forward
3
Score the misfit
candidate vs reference (lower is better)
4
Pick the best, report margin
best radius vs runner-up radius
loops until the misfit stops improving
Synthetic GPR-FDTD-FWI rebar inversion · status as of June 2026
2

## Slide 3
HOW IT WORKS
Forward simulation and inverse recovery
Synthetic GPR-FDTD-FWI rebar inversion · status as of June 2026
3

## Slide 4
HOW IT WORKS
Forward simulation and inverse recovery
Synthetic GPR-FDTD-FWI rebar inversion · status as of June 2026
3

## Slide 5
HOW IT WORKS
Radius ambiguity & confidence margin
Synthetic GPR-FDTD-FWI rebar inversion · status as of June 2026
3

## Slide 6
THE PIPELINE TODAY
Three workflow levels, one mature core
1 · Single-rebar
Detector-seeded local sizing
Detects one rebar, seeds an x/z/r refinement
Handles synthetic noise & source mismatch
Mature for local sizing — not a field claim
MATURE (LOCAL)
2 · Multi-rebar
Coordinate optimizer (the core)
3-rebar variable depth & radius
Bounded x/z/r search vs reference waveform
Reports geometry, radius, margin, diagnostics
MATURE CORE
3 · Field-data QC
Real GSSI data — import only
DZT import, metadata audit, sanity checks
Kept separate from synthetic experiments
No validated field inversion yet
QC STAGE ONLY
Synthetic GPR-FDTD-FWI rebar inversion · status as of June 2026
4

## Slide 7
STRONGEST RESULT
Exact geometry every time, across 425 runs
425
coordinate-optimizer runs parsed
425/425
selected the exact x / z / r
266/425
also cleared the strict cutoff
Acceptance fraction by target
Chart: 
| target0 (shallow-left) | target1 (center) | target2 (deeper-right)
Accepted % | 67.9 | 70.9 | 51.8
What the numbers mean
Localization is solved.
Every run picked the correct rebar geometry in the tested windows.
target2 is the most fragile
by confidence (51.8% accepted) even though its geometry is still exact.
Synthetic GPR-FDTD-FWI rebar inversion · status as of June 2026
5

## Slide 8
THE OPEN PROBLEM
The issue isn't location — it's confidence
159 of 425 exact-geometry runs stayed below the strict 5.0e-4 margin. The right rebar is found, but the best radius is sometimes only slightly better than the next competing radius.
Exact-geometry runs
Chart: 
| Accepted (clear) | Exact but weak
runs | 266 | 159
Why it happens
Two scenes that differ only slightly in radius can produce almost identical waveforms. The optimizer must separate them on a tiny misfit difference.
Why it's good practice
Confidence reporting flags the 159 weak rows instead of overstating certainty — it distinguishes exact-and-clear from exact-but-ambiguous.
Where it bites most
target2 (deeper, larger) is the most acceptance-fragile; target1 has exact-but-weak branches that resist simple escalation.
Synthetic GPR-FDTD-FWI rebar inversion · status as of June 2026
6

## Slide 9
RESCUE INTERVENTIONS
What rescues a weak run — and what doesn't
117 multi-run series tested three intervention families. The lesson: rescues are real but not monotonic — more is not always better.
Source-density
62 series
Often helps target2, but more sources can also worsen the margin.
Tx / Rx offset
33 series
Bracketing rescues acquisition-sensitive cases, especially target0.
Ringdown tuning
22 series
Stable when already in the right regime — not a universal rescue.
CONCRETE EXAMPLE · target2 source-density rescue (runs 1207–1209)
5 sources
margin 4.24e-4 weak
→
7 sources
margin 4.94e-4 near cutoff
→
9 sources
margin 5.60e-4 accepted
Synthetic GPR-FDTD-FWI rebar inversion · status as of June 2026
7

## Slide 10
STATUS
Confirmed, partial, and still open
CONFIRMED
Synthetic FDTD forward modeling
Single-rebar local refinement
3-rebar bounded coordinate optimization
Meaningful confidence reporting
Objective-variant diagnostics
PARTIAL
Source-density rescue policies
Tx/Rx-offset rescue policies
Ringdown050 replication near cutoff
target1 exact-but-weak handling
UNRESOLVED
Real GSSI field-data inversion
3D FDTD / FWI & 3D acquisition
Universal global optimizer
Synthetic → field threshold transfer
Coverage of older special cases
Synthetic GPR-FDTD-FWI rebar inversion · status as of June 2026
8

## Slide 11
RECOMMENDED NEXT STEP
A narrow decision pass — not another long marathon
The project is at a genuine stop-and-evaluate point. The next GPU run should answer one specific policy question, not broadly continue replication.
target1 weak branches
Decide when to use Tx/Rx bracketing instead of adding sources.
target2 near-misses
Decide when to escalate 5 → 7 → 9 source density.
Two cutoffs
Separate strict research confidence from practical reporting confidence.
Keep field data apart
Field-data experiments and trackers stay separate from synthetic.
Strongest result today: a mature synthetic inversion-and-reporting pipeline — not yet field-validated, not yet 3D.